## Slide 2
Kabul RNAV Visual & RNP-AR Process & Benefits
Roger Hall
RNAV Project Pilot
Emirates Airline

## Slide 3: Kabul RNAV Visual & RNP-AR Process & Benefits
©2015 Emirates. All Rights Reserved.
Real Scenarios – Increased Predictability
Capt Roger Hall
RNAV Project Pilot

## Slide 4: Overview
Emirates conducts many hundreds of procedures using FMS guidance and with visual reference to terrain. We call these “RNAV Visual” procedures
Why, How, Challenges & Benefits

## Slide 5: When do we Produce & use RNAV Visual?
Process only used in special cases, for approaches where visual reference to terrain by pilot is allowed & assured
Generally at isolated airports with special considerations
Not as a substitute for a state instrument procedure
Initiator is always safety, rather than efficiency (although we will explore efficiency as part of the process)

## Slide 6: Summary – RNAV Visual
Prefer automation used throughout RNAV Visual approach, to 500ft-1000ft AAL (rather than hand-flown) – enhances PF awareness of terrain and aircraft flight path
Weather minima selected are conservative – generally 2,500ft ceiling and 8km visibility (raised in areas of high terrain)
Offer most benefits at isolated airports with fewer facilities (rather than high-traffic, major international hubs)

## Slide 7: Scenario 1: no published approach
Kabul approach challenges
Rwy 29
Rwy 11
?
?
?
?

## Slide 8: Cockpit Video – Kabul Rwy 11

## Slide 9: Kabul – a number of challenges…
Centreline Rwy 11 – not possible
High airport elevation – 5,900 ft
High terrain – all sectors
Limited room to manoeuvre on approach to Rwy 11

## Slide 10: Kabul – a number of challenges…
30-degree offset Final – not possible – too steep path
Unpredictable military & civil traffic
Security concerns (flying south of airport not allowed)
Hot temperatures (3.5 degrees published baro VNAV vertical path becomes actual 3.7 degrees +)
Limited terrain data

## Slide 11: Kabul – a number of challenges…
Landing at max landing weight
Tailwinds
No internal guidance to assist pilot to Rwy 11
Pilot view on Downwind Rwy 11, looking toward runway

## Slide 12: Kabul – a number of challenges…
Pilot wonders: where should I turn Base?

## Slide 13: Kabul – a solution is produced…
Elements add up to unpredictable lateral & vertical approach paths to Rwy 11
Using; limited terrain data, simulator & live evaluation, Emirates developed & published a Company RNAV Visual chart (with associated FMS guidance)

## Slide 14: Kabul – a brief look at chart…

## Slide 15: Kabul – a look at pilot briefing guide…

## Slide 16: Kabul – Results…
Increased predictability (Pilot, Company & ATC)
Reduced rate of descent on Final
Increased safety for all
Reduced returns to home base without landing
Increased efficiency

## Slide 17: Scenario 2: FMS Guidance ends before Rwy Threshold

## Slide 18: Scenario 2: FMS Guidance ends before Rwy Threshold

## Slide 19: Scenario 2: No FMS Guidance to Rwy Threshold
Visual procedure - allows us freedom to do this

## Slide 20: Scenario 2: No FMS Guidance to Rwy Threshold
Pilot uses state chart, but with Company FMS coding and visual reference to terrain…

## Slide 21: Scenario 3: Published RNAV Visual approach

## Slide 22: Scenario 4: Published RNAV approach used as Baseline to Reduce Vertical Path Angle

## Slide 23: Scenario 4: Published RNAV approach used as Baseline to Reduce Vertical Path Angle

## Slide 24: Summary – RNAV Visual
Our experience has been; providing enhanced FMS guidance to pilots (within a safe and effective process) during a visual phase is nearly always better than providing no guidance at all
Results have shown increased predictability, lower rate of safety events, greater efficiency
Particularly helpful in reducing excessive bank angles, excessive rates of descent and unstable approaches
Less stressful for crew, enables them to better prepare for approach

## Slide 25: Kabul Rwy 29 ILS-to-RNP Missed Approach
©2017 Emirates. All Rights Reserved.
Enhancing Reliable Services to Kabul
Capt Roger Hall
RNAV Project Pilot

## Slide 26: Overview
Any approach minima below 7060 ft minima requires a 5.8% climb gradient instead of 3.3%
20-30 times a year, Emirates has to offload planned cargo from Dubai-Kabul, whenever the KBL forecast or reported cloud ceiling is below approx. 7,500ft to meet this gradient

## Slide 27: Solution
Using proven, regulator-approved principles and guidelines, Emirates paid to have special missed-approach design work done
Allows use of the existing ILS approach facility at Kabul, to lower minimums – with a lesser missed-approach climb gradient

## Slide 28: Solution
One of our main goals was minimum disruption to KBL ATC services – using the existing ILS for the approach portion achieves this
Regulator-approved design agency DFS (state provider for Germany) was retained for special terrain examination and design work

## Slide 29: Solution
Here’s a look at the full approach plate

## Slide 30: Development Process
Terrain & track analysis with special software
Performance analysis by Emirates specialists
Multiple Simulator evaluations
Certification from DFS

## Slide 31: Simulator Video – Kabul Rwy 29
Engine-out simulation

## Slide 32: Kabul Rwy 29 Missed Approach…
looking towards Rwy 11 – reverse path of missed approach
High airport elevation – 5,900 ft
High terrain – all sectors
Limited room to manoeuvre on missed approach to Rwy 29

## Slide 33: RNP-AR Missed Approach…
Using; certified capability of the Boeing 777 (down to RNP 0.11) Emirates developed & published a new missed approach procedure with an RNP value of 0.14

## Slide 34: Kabul – Results…
Increased landing predictability (Pilot, Company & ATC)
Fewer diversions
Reduced load on ATC (due to missed approaches & diversions)
Reduced returns to home base without landing
Little-to-no ATC training required – just awareness

## Slide 35: How can we Encourage Landings on the Correct Surface?
Should we progress, away from “100% visual” approaches?

## Slide 36: Is “RNAV Final” Clearance a Possible Solution?

## Slide 37: Summary
RNAV query toward enhancing safety?
Please contact:
roger.hall@emirates.com
roger@xflashsystems.com